## Slide 1
Fast Restoration Signaling in Optical Networks
Radim Bartos and Swapnil Bhatia
Dept. of Computer Science
http://www.cs.unh.edu/cnrg/
InterOperability Lab
http://www.iol.unh.edu/
Univ. of New Hampshire

## Slide 2
Application of OBS to restoration signaling
  Serial scheme (Fast Re-route)
  Parallel scheme
Modeling restoration signaling for evaluation
  Data Plane (Optical Transport Network) and
  Control Plane (Data Communication Network)
Evaluation
  Experimental design
  Results
Objectives Achieved
Bartos, R., Bhatia, S.
1
Notes: Let me begin by giving you a brief overview of the three most important aspects of our study. We can think of these as the objectives accomplished during this study. The motivating goal for this work, was to investigate whether OBS could be applied to achieving fast interim restoration. This is the key idea or focus or contribution of our work. To demonstrate this, we redesigned some of the current restoration schemes into OBS variants. But, to realize these schemes, and study them in a practical context, we needed a model of the control and data planes. So, we adopted a simple two-network model for the traditional control and data planes, i.e., control messages traverse a separate control network (which is a conventional IP inter-network) and the data is transported by a high bandwidth all-optical network. Once we had this mental picture, we could easily reformulate our OBS-based schemes in context of this model. So with that, we had everything we needed in order to evaluate our hypothesis that OBS-based schemes were faster than their non-OBS cousins. So we then attempted to calculate analytically, the total time required for restoration, i.e. for resuming data transport after failure. But it turned out that although and because our model was simple and sufficient, it did not lend itself well to analytical investigation. It proved difficult to model the exact signaling latencies in the control network, without making rather strong assumptions. So, that’s when we decided to measure and compare our OBS-based schemes with the current schemes, experimentally. We designed some basic experiments and gathered some initial results which we report in our paper.

## Slide 3
The Problem of Restoration
Two-network architecture
Current activation schemes
Role of OBS
Analytical modeling
Experimental setup
Discussion of results
Summary
Agenda
Bartos, R., Bhatia, S.
2
Notes: Given this background, we can now discuss each aspect in greater detail. I would like to proceed according to this outline. First, I would like to talk briefly about our view of the problem of restoration.

## Slide 4
Restore data transport after failure efficiently with minimum data loss
Trade-offs between conflicting requirements
  Restoration time, resource efficiency, scalability, restorability
Minimize data loss
  Fast re-routing of affected flows
    Relatively long-lived solution
    Optimal route computation or pre-reservation and signaling
  Fast interim transport of blocked, mission-critical data
  Network should make best effort to minimize data loss
The Restoration Problem
Bartos, R., Bhatia, S.
3
Notes: Roughly, the goal of the restoration process is to resume data transport efficiently after a failure with minimum disruption. There are many different metrics on which a solution to the problem of restoration can be evaluated. One of the references discusses them in greater detail. Restoration time, capacity efficiency and scalability are perhaps the most important ones in the list. As with many other multi-objective problems, these metrics conflict with each other and lead to some complex tradeoffs. The obvious one is the one between resource efficiency and restoration time. If we pre-compute, duplicate and pre-reserve the resources required for a particular traffic flow, then we can accomplish restoration at SONET-like timescales. For this study, we decided to focus on restoration time without any pre-reservation of resources, but with pre-computation of alternate path route. Depending on how much we can pre-compute before and about any possible failure, we can provide an efficient and optimal solution. However, any such scheme will require computation and information about the current state of the network. This will slow down restoration. Additionally, this leads to an ungraceful, all-or-nothing solution in the sense that while the restoration scheme figures out the optimal and long-term solution, the network is subjected to severe service degradation. So, we tried to focus on a somewhat “best-effort” but fast and interim solution. This leads to a much more graceful degradation of service where after a failure, the network switches from guaranteed transport to at least best-effort delivery, which is a much more desirable behavior.
Given these requirements, we need a model or an architecture to describe the context for any proposed solution. In our study, we came across some prior work by Austin, Doshi and others from Bell Laboratories.

## Slide 5
Control
(DCN)
Two-Network Architecture
Data
(OTN)
egress
ingress
Bartos, R., Bhatia, S.
4
Notes: They discuss this two-layer model of an all-optical network. The control network which they call the Data Communication Network is a low bandwidth, conventional IP network. All control elements reside in this network. All control messages traverse this network. The data network or the Optical Transport Network is a separate network consisting of relatively less-intelligent elements such as optical cross-connects and other devices. The OTN is cut-through and wavelength routed, and is only responsible for providing raw bit transport. It is thus truly transparent. We assume that a request for light path setup arrives with a primary and an alternate path. The ingress DCN node then initiates the signaling process for the primary light path and also propagates necessary information about the alternate path.

## Slide 6
(OTN)
Control
(DCN)
Two-Network Architecture
egress
ingress
Serial Activation
Fast Re-route with
Bartos, R., Bhatia, S.
5
Notes: This shows, an example. At each step, neighboring nodes exchange port and wavelength information and initiate a cross-connect operation. This is a SERIAL path activation scheme because the signaling messages travel in series along the path from one DCN node to another. We apply this activation scheme to a well known restoration technique known as Fast Reroute. For example, the primary path is setup up as shown and a link fault occurs. The node downstream to the failure detects the failure. Using serial activation, a reverse path to the ingress is first setup. Then, the ingress activates the remaining forward segment of the alternate path. This is Fast Reroute with Serial Activation.

## Slide 7
(OTN)
Two-Network Architecture
egress
ingress
Parallel Activation
Fast Re-route with
Bartos, R., Bhatia, S.
6
Notes: In contrast, in a parallel activation scheme, the ingress DCN node multicasts the signaling message to all the other nodes on the path, simultaneously. Here’s an example. In the next step, neighboring nodes exchange port and wavelength information, and finally the cross-connect is instructed to make the necessary connection. There may be other variants of this scheme with different levels of pipelining-parallelism. Let’s look at the fault scenario in the parallel case as well. Once a fault occurs, the egress will detect it, through a loss of signal. In this case, the egress itself initiates the alternate path activation operation. However, we observe that both the activation schemes involve signaling over a fairly large control network. This leads to long round-trip delays since each setup message needs to wait for an acknowledgement. Our paper contains analytical estimates of the total time required to complete the activation process in both the serial and parallel case and it shows that even with some simplifying assumptions, the two way round-trip delay for each message remains the the largest contributor to the total restoration time.
With this preliminaries, we are now in a position to enhance these existing schemes by re-implementing them as burst-switched schemes.

## Slide 8
Tell-and-go, one-way reservation protocol
Control packet configures cross-connects along the path
Data burst follows with sufficient delay
No setup acknowledgement
  significant reduction in setup time
  quick, bulk transfer
  flexible resource utilization
  burst may be dropped
control and data channels may or may not be separate
Optical Burst Switching (OBS)
Bartos, R., Bhatia, S.
7
Notes: Optical Burst Switching belongs to a family of bandwidth arbitration protocols known as “tell-and-go” or one-way reservation protocols. A client who wishes to send data requests bandwidth by sending a control message ahead of time containing the time and length of the actual data. Then, at the pre-decided time, the client sends the data burst without waiting for any acknowledgement. This has many important implications: the most relevant of them being that the OBS allows a client to send large amounts of data with very small setup latency. We claim, that this makes it ideal for application as an alternate path activation technique. Although we do not discuss it in this study, we also believe that OBS also allows us enough flexibility to design smarter schemes for transporting data away from the failure, quickly. A drawback of this scheme is that since we do not wait for an acknowledgement, it may so happen that enough resources were unavailable somewhere along the path because of which a path was not established successfully. However, considering real-world networks built for deploying mission-critical applications, we believe that that such an OTN would be over-built to allow sufficient redundancy for restoration. Hence, the probability of a burst being dropped due to lack of resources can be minimized to an acceptable level.
Next we apply OBS to the serial activation scheme discussed earlier.

## Slide 9
(OTN)
Control
(DCN)
Serial Activation with OBS
egress
ingress
cntrl
data
t2
t3
t4
@t3
t1
@t4
Bartos, R., Bhatia, S.
8
Notes: Again, lets assume the primary path is setup and a link failure occurs. As seen earlier, the downstream node detects the failure and generates an alarm. At this point, the DCN node constructs the OBS control packet containing port, wavelength and timing information. In general OBS control packets refer to burst times in the future, but here we make the necessary assumption that the burst needs to be sent as soon as possible. Each DCN node receives this packet and forwards it to the next node with updated port/wavelength information. Lets assume the control packet takes time t1 to reach node 1, t2 to reach node 2 aznd so on. Also, lets assume that the time to configure the cross connect is small compared to the ti. So, at time t3, the segment of the path shown in the OTN is already configured and ready for use. Note that the segment only extends till before node 3 in the OTN. Similarly, at time t4, the segment shown is extended and is available for use. Again, it is usable only till before node 4 in the OTN. Thus, as long as we ensure that the data burst does not arrive at a cross connect BEFORE the control packet arrives at its corresponding DCN node, we can start sending data BEFORE the entire path is configured. To ensure this, we start sending data after a delay ‘d’. To find out the constraint on ‘d’, we layout the problem as follows:

## Slide 10
Serial Activation with OBS
For all s: ts < Os
ts < d + Os
ts – Os < d
Bartos, R., Bhatia, S.
9
Notes: As in the previous slide, let us assume that it takes time ti for the control message from the initiating DCN node to reach DCN node i over the DCN. In addition let us assume that it takes time O_i for the data burst to arrive at an OTN cross connect. So, we would like to ensure that in no case, does the burst arrive at a switch before the control message, again, allowing a relatively small amount of time for cross-connect configuration. That is, we want to ensure that tn > On for all nodes. If we send the data burst after delay d, then it will take d+On to reach a cross connect. So, the condition then becomes: which can be written as:. Since this condition must be enforced over all ‘n’, we need to set ‘d’ larger than the maximum of value over the path.

## Slide 11
(OTN)
Parallel Activation with OBS
egress
ingress
cntrl
data
t2
t3
t4
@t1
t1
@t5
t5
t6
t7
time
@t3
Bartos, R., Bhatia, S.
10
Notes: Again, lets assume the primary path is setup and a link failure occurs. As seen earlier, the egress node detects the failure and generates an alarm. At this point, the DCN node constructs the OBS control packet containing port, wavelength and timing information. Lets say the control message reaches the DCN nodes on the alternate path at times t1, t2, .. t7. However unlike the serial case, there is no obvious ordering among t1, t2 etc. lets assume the distances on the slide are to scale, then t3 is the farthest followed by t4, and so on. Thus, we can draw the following compartments. So, the message reaches t7 first, followed by t6 and t1 and so on. Now, if we see the state of the light path at time t1 then we will see that it gets built in fragments. Only this particular fragment is setup. Next, at t5, this fragment is built and so on. Nonetheless, if we try to formulate the constraint, we see that it remains the same as in the serial case.

## Slide 12
Parallel Activation with OBS
For all p: tp < Op
tp < d + Op
tp – Op < d
Bartos, R., Bhatia, S.
11
Notes: Again, we want to find the delay ‘d’ by which to delay the burst such that the burst always reaches a cross-connect after it has seen the control packet. From the figure is should be easy to see that:

## Slide 13
The Problem of Restoration
Two-network architecture
Current activation schemes
Role of OBS
Analytical modeling
Experimental setup
Discussion of results
Summary
Agenda
Bartos, R., Bhatia, S.
12
Notes: We tried to capture the latency of the DCN analytically and some simple results are described in the paper. However, it proved difficult to capture the delay without making any simplifying assumptions.

## Slide 14
(OTN)
Two-Network Architecture
egress
ingress
Parallel Activation
Fast Re-route with
h
Bartos, R., Bhatia, S.
13
Notes: For example, when we look at the parallel-activation, then there is no simple way of modeling the latency that the control message is subjected to. We assumed that each DCN node was a constant ‘h’ hops away from each other, but this may not really capture the real model. So we followed the alternate route of empirically evaluating our proposed schemes.

## Slide 15
The Problem of Restoration
Two-network architecture
Current activation schemes
Role of OBS
Analytical modeling
Experimental setup
Discussion of results
Summary
Agenda
Bartos, R., Bhatia, S.
14
Notes: We tried to capture the latency of the DCN analytically and some simple results are described in the paper. However, it proved difficult to capture the delay without making any simplifying assumptions.

## Slide 16
Generate a set of 10 pairs of networks with random topologies over definite geographical sizes to represent the OTN and DCN.
  All OTN topologies 2-vertex connected
  All DCN topologies transit-stub (Internet-like)
  Edge weights represent geographical distances
Generate a geographically sound 1-1 mapping between control nodes in the DCN and corresponding OTN nodes.
For all pairs of nodes in the OTN generate the shortest and second-shortest path.
Assume that a link-fault occurs mid-way on the primary path
For all pairs of networks, for all paths, for all activation schemes calculate time to setup alternate path and total time for restoration
Perform (5) for varying network size, path length and connectivity.
Experimental Design
Bartos, R., Bhatia, S.
15
Notes: Our goal was to compare the performance of our proposed schemes against their non-OBS counterparts. We laid out the following plan: First, we generated a set of 10 pairs of random networks using the Georgia Tech. Internet Topology Modeler (gtitm). GTITM allows you to generate random graphs with several different characteristics. It allows control over various attributes such as number of nodes in the graph, number of edges, probability of an edge between nodes, geographical size of the graph and structural attributes such as number of levels of hierarchy and its type. We used a flat random model model to represent the OTN and a transit stub model to represent the DCN. We chose the OTN and DCN to be over the same geographical size (100milesX100miles). The random topologies generated contained weights on the edges which represented real distances according to the area over which the graph was defined. Next, we created a mapping between a node in the OTN to a node in the DCN which was closest to it in Euclidean distance. Thus, we created the two-network model with a DCN node controlling every OTN node. In most of the experiments, the OTN was much smaller in size (node-count wise) than the DCN. Then for each OTN, the shortest and the second-shortest paths were generated. The shortest path was taken to be the primary path and the second-shortest path was taken to be the secondary path. We assumed the occurrence of a failure mid-way on the primary path and calculated the time to setup the alternate path using all four schemes. With this time, we were able to calculate the total time for restoration using all four schemes. This experiment was repeated for varying network size (node-count), varying geographical size, varying path length and varying connectivity.

## Slide 17
Georgia Tech. Internet Topology Modeler
  Pure-Flat random – OTN
  Transit-stub – DCN
The Stanford GraphBase (SGB)
  C library of routines to manipulate graphs
  GTITM based on SGB
CAIDA “Walrus” Visualizer
Experimental Design
Bartos, R., Bhatia, S.
16

## Slide 18
The Problem of Restoration
Two-network architecture
Current activation schemes
Role of OBS
Analytical modeling
Experimental setup
Discussion of results
Summary
Agenda
Bartos, R., Bhatia, S.
17

## Slide 19
Based on the total time to restore metric:
Serial schemes worse than parallel schemes
OBS schemes much (twice as) better than non-OBS schemes
  Serial OBS better then serial
  Parallel OBS better than parallel
Parallel schemes much more resilient than serial schemes to
  network size
  alternate path length
Results
Bartos, R., Bhatia, S.
18

## Slide 20
Results
Alternate Path Length v/s restoration time
Bartos, R., Bhatia, S.
19
Notes: Lets briefly look at the results of one of the experiments. In this case, the variation of restoration time was measured with respect to path length. Thus, the restoration time for paths of length 1, 2, 3 … were calculated for the random OTN-DCN pairs generated. X axis shows the path length, the left-Y axis shows the restoration time. The right-Y axis shows the number of paths of a particular length that were used in the measurement. The first line represents the serial scheme without OBS. The green line represents the serial scheme but this time with OBS. As you can see, the OBS scheme is almost twice as fast as the non-OBS scheme, as expected. Similarly, for the parallel schemes, OBS does better than non-OBS, again almost twice as fast. However, the difference is not large, since for the parallel case the burst delay is regulated by a more constrained condition. Also, these are for the shortest and second shortest paths. It would be interesting to see the result when a path that minimizes restoration time for all the methods is chosen as the alternate path, which may not be the shortest path (tn-On). Also, as expected, the parallel schemes are much more resilient to path length than serial schemes because of the connected nature of the internet-like DCN.

## Slide 21
Application of OBS to restoration signaling
Modeling restoration signaling for evaluation
Evaluation
Use restoration time as metric for choosing alternate path
Modeling internetworks for studying fault-tolerance
  Faloutsos et. al
  Genetic algorithm
Multi-homing and fault-tolerance
Summary
Bartos, R., Bhatia, S.
20
Notes: So in closing, I would like to summarize: The project started with the novel idea of applying optical burst switching to speed up restoration signaling. We applied the idea to serial and parallel schemes of activation. We modeled the restoration architecture as a two separate networks: one for signaling and the other for data. And we experimentally verified the hypothesis that the OBS schemes perform better than non-OBS schemes.
We are also working on some new ideas: one that I mentioned in passing was to choose the alternate path such that restoration time would be minimized. So the restoration time becomes the metric on the basis of which a path is deemed shortest or best. Another area of exploration is modeling internet-works for studying and introducing fault-tolerance and robustness. This work started with the paper by Faloutsos and others which characterizes the Internet as a scale free or power law network. We are also studying whether an evolutionary approach can help build a better and more robust network. And lastly, we are looking at studying some specific problems in connection to fault-tolerance such as multi-homing and how it can be exploited to guarantee robustness.